## Slide 1
SPANviewer - A Visualization Tool
16/05/2013
Stefan Kimmer
for Advanced Robotics Applications

## Slide 2
Outline
SPANviewer | Stefan Kimmer | ESA Telerobotics and Haptics Laboratory

## Slide 3: Outline
Motivation
Software – Architecture and Concepts
Current Applications
Conclusion

## Slide 4
Motivation and Requirements
SPANviewer | Stefan Kimmer | ESA Telerobotics and Haptics Laboratory

## Slide 5: Motivation and Requirements
Motivation
Generic viewer for serial and parallel robotics
Requirements
Cross platform
Conventions as commonly used in robotics, e.g.:
    Denavit-Hartenberg parameters
    Frames (Position + Euler angles)
  Quick debugging and analysis of control algorithms
    E.g. Quick configurable communication
  Overlay of virtual robotic structures in video streams
  Stereoscopic (3D) visualization for passive stereoscopic displays

## Slide 6: Motivation and Requirements
Requirements
Requirements
Integration in the Space Portable Applications Network (SPAN)
    SPAN: developed at ESA
=> SPANviewer

## Slide 7
Software
Architecture and Concepts

## Slide 8: Software Architecture and Concepts
Software Architecture
Built on top of open source libraries
All libraries are cross platform
Written in C++
The SPANcomm library: for inclusion in the SPAN tool chain

## Slide 9: Software Architecture and Concepts
Software Concepts
One XML file as input which contains definitions for a world
    The world contains definitions for a scene
      In the scene robotic structures and other objects can be defined
    The XML file can define which parts can be controlled by a communication interface
    A camera (viewpoint) or multiple cameras can be defined
  Communication through UDP messages and shared memory
    Without the need of a custom protocol

## Slide 10: Software Architecture and Concepts
Sotware Concepts – the XML file
Scene Definition
Robotics structures
    E.g.: Parallel structure
<?xml version="1.0"?>
<world xmlns="ESA-Telerobotics-Lab-SPAN">
<scene units="0.2">
<structure convention="dh">
<joint d="0.5“ theta=“0” a="0" alpha="-1.5708" />
<joint d="0“ theta=“0” a="0.5" alpha="1.5708" />
</structure>
</scene>
</world>
=> Denavit-Hartenberg parameters: d, , a,
Input
One XML file as input
    World as root element

## Slide 11: Software Architecture and Concepts
Sotware Concepts – the XML file
Scene Definition
Series structure
    The hierarchical nature of the XML allows straight forward kinematic chaining
<?xml version="1.0"?>
<world xmlns="ESA-Telerobotics-Lab-SPAN">
<scene units="0.2">
<structure convention="dh">
<joint d="0.5“ a="0" alpha="-1.5708" >
<joint d="0“ a="0.5" alpha="1.5708" />
</joint>
</structure>
</scene>
</world>

## Slide 12: Software Architecture and Concepts
Sotware Concepts – the XML file
Camera
Defines a view point
Opens a separate window
<?xml version="1.0"?>
<world xmlns="ESA-Telerobotics-Lab-SPAN">
<camera>
<monocamera window_title="monocamera X">
<pose x="100" y="0" />
</monocamera>
<monocamera window_title="monocamera Y">
<pose x="0" y="100" />
</monocamera>
<stereocamera>
<pose x="700" z="200" z="0" />
<screendef diameter="1016" />
</stereocamera>
</camera>
<scene units="100">
<cube sx="100" sy="10" sz="20" tx="200“>
</scene>
</world>

## Slide 13: Software Architecture and Concepts
Sotware Concepts – Coomunication
Communication model
Low level Protocols: UDP or Shared Memory
Each object can use a different channel
<?xml version="1.0"?>
<world xmlns="ESA-Telerobotics-Lab-SPAN">
<scene>
  <structure convention="dh" channel=“2">
    <joint a="10" alpha="0">
    <joint a="20" alpha="1.5708" />
    </joint>
  </structure>
  <cube channel=“1"/>
</scene>
</world>
xml.xml
> spanviewer --input xml.xml --channel 25001 25000
Command line execution:
import socket, struct
sock = socket.socket(socket.AF_INET, socket.SOCK_DGRAM)
sock.sendto(struct.pack("ddd", 11, 12, 0), ("127.0.0.1", 25001))
Sending position values to the cube with Python:
Sending joint values to the structure with Simulink:
Port 25000

## Slide 14: Software Architecture and Concepts
Sotware Concepts – Video Streams
Video Streams
Embedded as
    Image in the scene
    Background image
Send to it via an image channel
> gst-launch autovideosrc ! ffmpegcolorspace ! video/x-raw-rgb, width=1920, height=1080, bpp=24 ! shmsink shmkey=Overlay
Command line to launch a stream of camera video with GStreamer to the SPANviewer:
<?xml version="1.0"?>
<world xmlns="ESA-Telerobotics-Lab-SPAN">
<scene>
<backgroundimage resx="1920" resy="1080" channel=“1” />
</scene>
</world>
xml.xml
> spanviewer --input xml.xml --img-channel Overlay
Command line execution:
Output

## Slide 15
Current Applications

## Slide 16: Current Applications
Kinematic Studies
Controlling a simulation of the KUKA light weight robot with 7 joints by an exoskeleton
    Enables the study of kinematic mapping
    Elbow control algorithms can be analyzed

## Slide 17: Current Applications
Kinematic Studies

## Slide 18: Current Applications
Overlay of Video Streams
Virtual overlay for enhancing situational awareness
Internal camera parameters can be configured
External camera parameters can be sent in real time

## Slide 19: Current Applications
Overlay of Video Streams

## Slide 20: Current Applications
Stereoscopic Augmented Reality
Enhancing Situational awareness
Visualizing a force vector at the point of exertion at the real robot
View point adaption for the operator

## Slide 21: Current Applications
Stereoscopic Augmented Reality

## Slide 22
Conclusions

## Slide 23: Conclusions
SPANviewer fully implemented and tested
    Easily adaptable modeling
    Used as a debugging tool
    Variety of applications in the Telerobotics and Haptics Lab
  Easy deployment
    Working on different OS (Linux PC, Windows both PC and tablet)
    End-user installer/package

## Slide 24
Thank you!
Questions?
SPANviewer – A Visualization Tool for Advanced Robotics Applications
Stefan Kimmer1,2,3, João Rebelo1,2,3 and André Schiele1,2,3
1 E-mail: {stefan.kimmer, joao.rebelo, andre.schiele} @ esa.int
2 Faculty of Mechanical, Maritime and Materials Engineering, Delft University of Technology, Delft, The Netherlands
3 Telerobotics and Haptics Laboratory, ESTEC, Noordwijk, The Netherlands